## Slide 1: Thrustmaster
CASE STUDY PRESENTATIONS
CASE STUDY 3 | WORKING GROUP-3
Lean Transformation: From Job Shop to Flow
Lean Manufacturing + Flow + Standard Work
Presented to:
Course Faculty
Presented by:
Group No. WG-3 | Section O1
1. Arpit Shukla | 246213322
2. Yash Vardhan Chauhan | 246213008
3. Tasleen Kaur | 246213168
4. Naman Khatri | 246213334
5. Manu R | 246213066
6. Abhinav Dongre | 246213406
Business Operations Excellence
Notes: Introduce the group (WG-3, Section O1) and the case: Thrustmaster's Lean transformation, themed Lean Manufacturing + Flow + Standard Work. Management's question: how do we turn a complex job shop into a visible, stable, efficient flow system without losing product flexibility?

## Slide 2: COMPANY BACKGROUND
A Houston-based, engineer-to-order maker of marine propulsion, where one late thruster can hold up a whole ship.
Who are they?
Thrustmaster of Texas: family-owned manufacturer founded by Joe Bekker in Houston, Texas
Fast growth: revenue up >1,000% and staff up ~700% in about a decade
One large plant with fabrication, machining, assembly and testing
What do they do?
Design and build marine propulsion: tunnel, azimuth and retractable thrusters, portable and outboard units, hydraulic power units
Engineer-to-order: similar build steps, but every job router (100+ pages) changes with the customer's spec
Why is the operation important?
Propulsion is mission-critical: a vessel can't sail or hold position without it
Thrusters sit on the shipyard's critical path, so a late unit delays the vessel
High value, low volume: delivery, quality and cost drive margins
+1,021%
revenue growth over 10 years
+700%
growth in staff over 10 years
~200k sq ft
factory floor
100+ pages
in a single job router
Sources: LEI Lean Transformation Summit 2016, "Propelling Ahead: Thrustmaster of Texas' Lean Journey"; LEI, "Thrustmaster Comes Around" (2016); trade press on company history.
Notes: Who: Thrustmaster of Texas, a family-owned Houston manufacturer founded by Joe Bekker. What: engineered marine propulsion (tunnel, azimuth and retractable thrusters, portable/outboard units, HPUs). Each unit is built to customer spec, so job routers can run past 100 pages. Why it matters: thrusters are on the shipyard's critical path, so lateness costs the customer a vessel schedule. Rapid growth (revenue +1,021%, staff +700% in ~10 years) is what stretched the job-shop model.

## Slide 3: BUSINESS PROBLEM
What was going wrong? A fast-growing job shop that couldn't see its own work, so it couldn't control it.
COST
Project costs above target (>100%)
Overtime and extra labour added just to ship
WIP and rework tie up cash and margin
QUALITY
~50% first-pass yield (est., Q1 2014)
Defects found late, at test, then reworked
Quality inspected in, not built in
DELIVERY
~20% on-time delivery (Q1 2014)
ERP scheduling, an APS system and new machines didn't fix it
No visible work status, so expediting = firefighting
PRODUCTIVITY
~7 miles and ~10 h of waste per unit
Technicians walk to find parts, tools and information
Schedule attainment only ~30%
CUSTOMER
Unreliable promise dates
Late thrusters disrupt shipyard build schedules
Trust and repeat business at risk in a niche market
EMPLOYEE
Know-how locked in a few heads
Undefined work areas, little standard work
Hard to train new hires while headcount grew ~700%
Metrics: LEI Summit 2016 deck (Q1 2014 baseline) and LEI spaghetti-chart study. Customer and employee impacts: WG-3 analysis.
Notes: Walk through the six lenses. The headline numbers come from LEI's Thrustmaster material: on-time delivery around 20% and first-pass yield around 50% in Q1 2014, project costs above target, schedule attainment around 30%, and a spaghetti chart showing roughly 7 miles of walking and nearly 10 hours of non-value-added time per unit. Point out that software and machines were tried first and did not work. The problem was the system, not the tools.

## Slide 4: CURRENT STATE PROCESS
Before: MRP pushes every order through shared functional departments, and work queues everywhere.
WIP / queue
Push movement
Production Control: MRP / ERP + APS
push schedules to every department
Suppliers
Customers
Receiving & Stores
Machining
Fabrication & Weld
Assembly Bays
Test, Paint & Ship
I
I
I
I
I
I
Material arrives in MRP batches
Parts not kitted; techs search for material
MRP batches queue for every product
Shared by all products; long waits
Units built in place; techs walk for parts & tools
Defects found late, then reworked upstream
Only ~20% of orders on time
~7 mi
walked per unit (spaghetti chart)
~10 h
non-value-added time per unit
~20%
on-time delivery
(Q1 2014)
~50%
first-pass yield
(Q1 2014)
Managers couldn't see:
WIP
Finished goods
Work status
Labour requirements
Process flow
Data: LEI (2016): spaghetti chart and Q1 2014 metrics. Process map simplified by WG-3 for illustration.
Notes: This is the 'Before' picture. Production control runs MRP/ERP plus an APS tool and pushes schedules to every functional department. Each product takes its own path through stores, machining, fabrication, assembly bays and test, and WIP piles up between them. Technicians build units in place and walk to fetch parts and tools: about 7 miles and 10 hours of waste per unit. Managers could not see WIP, finished goods, work status, labour needs or the process flow.

## Slide 5: WASTE IDENTIFICATION: THE 8 WASTES (TIMWOODS)
~10 hours of non-value-added time per unit: the problem was waste in the system, not a lack of effort.
T
Transportation
Heavy housings and parts move between far-apart departments
Fix: Cells by product family
I
Inventory
WIP piles in every department; nobody can count it
Fix: FIFO lanes with WIP caps
M
Motion
~7 miles of walking per unit for parts, tools and drawings
Fix: Kits and defined work areas
W
Waiting
Units wait for missing parts, the crane, the test stand or decisions
Fix: 3-day pitch; kit complete before start
O
Over-production
MRP batches build parts ahead of need
Fix: Pull: build what the next step needs
O
Over-processing
Re-reading 100+ page routers; repeated checks and workarounds
Fix: Standard work for common steps
D
Defects
~50% first-pass yield; errors caught late at test
Fix: Built-in quality checks at each station
S
Skills (unused talent)
Know-how sits with a few experts; operators not engaged in improvement
Fix: Standard work + daily huddles
Walking and FPY figures: LEI (2016). Waste examples and fixes: WG-3 analysis of the case.
Notes: Map each of the eight wastes to what we saw at Thrustmaster, and give the Lean fix that answers it. The biggest are motion (about 7 miles of walking per unit), inventory (WIP nobody could count), waiting, and defects (about 50% first-pass yield). Unused talent matters too: expert knowledge was never written down, which is what standard work fixes.

## Slide 6: ROOT CAUSE ANALYSIS: FISHBONE (6M)
Causes cluster in method, layout and information, not in people's effort.
EFFECT
~20% on-time delivery and ~50% first-pass yield
METHOD
No standard work: each tech builds 'their way'
MRP push scheduling and batch release
MATERIAL
Parts not kitted; shortages found at assembly
Raw stock and WIP piles hide what's missing
PEOPLE
Tacit knowledge held by a few experts
Firefighting and overtime culture
MEASUREMENT
No visible WIP, status or takt
Defects detected late, at test
MACHINE
Shared cranes, machines and test stands create queues
New machines added; flow unchanged
LAYOUT
Functional job-shop layout
Undefined work areas; ~7 miles walked per unit
Notes: Fishbone across the 6Ms. The effect is late delivery and poor first-pass yield. Method: no standard work, MRP push. People: knowledge was tacit, and the culture ran on firefighting. Machine: shared resources created queues, and buying machines didn't change the flow. Material: no kitting, so shortages showed up at assembly. Measurement: nothing visible (WIP, status, takt), and defects were found late. Layout: a functional job shop with undefined work areas. Most causes are system-design causes.

## Slide 7: ROOT CAUSE ANALYSIS: 5 WHY
Asking 'why' five times leads past the symptoms to a system-design problem.
PROBLEM: only ~20% of orders shipped on time (Q1 2014)
WHY 1
Why are orders late? Units sit in queues waiting for parts, shared resources and rework.
WHY 2
Why do they queue? MRP pushes work into departments regardless of real capacity or sequence.
WHY 3
Why can't capacity be matched? Every job takes its own path through a functional layout, with no cadence and no visible status.
WHY 4
Why no cadence or visibility? Work areas, labour content and methods were never defined: no standard work.
WHY 5
Why no standard work? The shop ran on tacit knowledge and was organized around departments, not product flow.
ROOT CAUSE
Thrustmaster had no flow system. Layout, scheduling and work methods were organized by function and individual experience, not by product family and standard work.
So the fix must be systemic:
Flow layout: product-family cells
Standard work at every station
Pull + a 3-day pitch
Visual management and daily huddles
Notes: Five whys from the delivery problem. Late orders come from queues; queues come from MRP push without regard to capacity; capacity can't be matched because every job follows a different path with no cadence or visibility; that's because work areas and methods were never standardized; and that's because the shop ran on tacit knowledge, organized around departments rather than product flow. Root cause: there was no flow system. So the countermeasure has to redesign the system, not add more software or overtime.

## Slide 8: OPERATIONAL EXCELLENCE SOLUTION
What should management change? Stop managing departments and schedules; manage the flow of each product family.
1
Map the value stream
SEE THE WHOLE
VSM and spaghetti chart expose the waste and WIP
2
Reorganize by product family
PRODUCT FAMILIES
P-Q analysis groups drives by size and characteristics
3
Create assembly cells
FLOW
Co-locate people, parts and tools per family
4
Develop standard work
STANDARDIZATION
Capture expert know-how as posted sequences
5
Define work areas
VISUAL WORKPLACE / 5S
Every station, tool and WIP spot labelled
6
Introduce pull-based movement
PULL
Next step pulls; FIFO replaces MRP dispatch
7
Set takt / pitch
RHYTHM
A 3-day pitch shows progress every 3 days
8
Build quality into the process
JIDOKA
Checks at each station: stop and fix
MANAGEMENT BEHAVIOURS THAT MAKE IT STICK
Go to the gemba
Daily cell walks and 10-minute huddles
Leader standard work
Check the pitch board every 3 days
Keep flexibility
Standardize steps; let specs vary
Notes: These are the eight moves Thrustmaster made, each tied to a Lean principle: see the whole, product families, flow, standardization, visual workplace, pull, rhythm, and built-in quality. The management shift underneath is to stop managing departments and schedules and manage the flow of each product family instead. Leaders have to go to the gemba, follow their own standard work, and protect flexibility by standardizing the steps rather than the product.

## Slide 9: FUTURE LAYOUT: PRODUCT-FAMILY ASSEMBLY CELLS
Two size-based assembly cells fed by a kitting supermarket give short, visible, one-direction flow (illustrative layout).
Machining
kanban replenishment
Fabrication & Weld
kanban replenishment
Purchased parts
two-bin / supplier kanban
KITTING
SUPERMARKET
1 complete kit per drive, per pitch
CELL A: small / medium-frame drives e.g., tunnel thrusters
S1
Sub-assembly
S2
Drive / gearbox
S3
Final assembly
S4
Test & QC
Material moves every 3 days (pitch) · max. 1 drive in each FIFO lane
CELL B: large-frame drives e.g., azimuth and retractable thrusters (crane bay)
B1
Sub-assembly
B2
Main assembly (crane)
B3
Test & QC
Material moves every 3 days (pitch) · max. 1 drive in each FIFO lane
PAINT, PACK & SHIP
to the customer
Two cells by product size: similar work content, tooling and lifting needs
Defined work areas: marked stations, WIP and tool locations
Point-of-use kits: no trips to stores (target < 1 mile walked per unit)
One-direction flow with a visual pitch board at each cell
Notes: Future layout. P-Q analysis splits the drives by size into two families, and each gets its own cell: Cell A for small and medium-frame drives at benches, Cell B for large-frame drives in a crane bay. A kitting supermarket between machining/fabrication and the cells hands each cell one complete kit per drive per pitch, so technicians stop walking to stores. Flow runs one way to paint, pack and ship. This mirrors Thrustmaster's two size-based cell configurations; which products go to which cell is our assumption.

## Slide 10: FLOW: TAKT TIME AND THE 3-DAY PITCH
At low volume, takt is measured in days. A 3-day pitch moves every drive one station forward and finishes one drive every 3 days.
TAKT TIME
Available working time ÷ customer demand
Illustrative: 63 working days per quarter ÷ 21 drives = 3 days per drive
PITCH
The interval for releasing and moving work: 3 days. Each pitch, every drive moves one station forward.
EVERY 3 DAYS AT THE PITCH BOARD
Material moves to the next station
Cell lead checks plan vs. actual
Misses escalated and fixed within the pitch
Pitch board, Cell A (illustrative)
Station | Pitch 1 Day 0–3 | Pitch 2 Day 3–6 | Pitch 3 Day 6–9 | Pitch 4 Day 9–12 | Pitch 5 Day 12–15
S1 Sub-assembly | D1 | D2 | D3 | D4 | D5
S2 Drive / gearbox |  | D1 | D2 | D3 | D4
S3 Final assembly |  |  | D1 | D2 | D3
S4 Test & QC |  |  |  | D1 | D2
Completed |  |  |  | D1 ✓ | D2 ✓
1 drive / 3 days
steady output once the cell is full
4 drives
fixed WIP in the cell, one per station
12 days
in-cell lead time per drive (4 pitches)
Problems now surface within one pitch (3 days), not at month-end when the order is already late.
Notes: Flow. Takt is available time divided by demand; for engineered drives it comes out in days, not seconds. Thrustmaster used a 3-day pitch: every three days a drive is completed and material moves to the next station. The board shows drive D1 stepping through S1 to S4 one pitch at a time; from pitch 4 on, one drive finishes every 3 days. WIP is fixed at four drives per cell, and any miss is visible within 3 days. The 63-day / 21-drive numbers are illustrative.

## Slide 11: STANDARD WORK: FROM TACIT KNOWLEDGE TO A SHARED BEST WAY
The assembly steps are roughly the same for every unit; only the specs change. Standardize the steps and let the router carry the specs.
THE 3 ELEMENTS OF STANDARD WORK
Takt / pitch time
The pace: each station finishes its work within the 3-day pitch
Work sequence
The best-known order of steps, with key points for quality and safety
Standard WIP
One drive at each station plus at most one in each FIFO lane
SUPPORTING TOOLS
Job breakdown sheets (TWI) to train new hires
Standard work posted at every station
Time-based operations visible on the pitch board
Leader standard work for supervisors
Standard work sheet, Cell A, Station S2: drive / gearbox assembly (illustrative)
# | Work element | Key point (quality / safety) | Time (h)
1 | Verify kit against router and spec sheet | Kit 100% complete before starting | 1.0
2 | Install bearings and seals in housing | Press to depth; no seal damage | 5.0
3 | Assemble gear set; set backlash | Record backlash on check sheet | 7.0
4 | Torque fasteners to spec | Calibrated wrench; torque stripe | 3.0
5 | Pressure / leak test sub-assembly | Fail = stop and call the cell lead | 4.0
6 | Self-check, sign off, move to FIFO lane | Only good units move forward | 1.0
 | Total work content | ≤ 24 h available per 3-day pitch (1 shift) | 21.0
New hires productive faster
Less variation, so FPY rises
Labour need visible per cell
A baseline for kaizen
Notes: Standard work has three elements: the pace (the pitch), the sequence, and standard WIP. Thrustmaster's insight was that the assembly steps are roughly the same for every unit; only the customer details in the router change. So standard work fixes the steps and key points, and the router supplies the specs. The sheet on the right is an illustrative example: total work content of 21 hours fits inside the 24 hours available in a 3-day pitch on one shift. That is how standard work also makes the labour requirement visible.

## Slide 12: PULL SYSTEM: FIFO, KITS AND VISUAL SCHEDULING
Replace MRP dispatch with visual pull: work starts only when the next station is ready, so WIP stays capped and easy to count.
Material flow
Pull signal
Suppliers
Machining & Fab
Kitting supermarket
ASSEMBLY CELL (pacemaker)
S1
S2
S3
S4
Test & Ship
Customer
VISUAL FIFO SCHEDULE
the only scheduling point
release 1 kit per pitch
customer orders, by due date
kit pull
kanban
two-bin kanban
FIFO lanes with a cap
At most 1 drive waits between stations. If the lane is full, upstream stops and helps.
Kit before you start
The supermarket issues a complete kit per drive per pitch. No partial starts.
Kanban for common parts
Two-bin kanban for fasteners, seals and bearings; custom parts are ordered against the drive.
One scheduling point
Only the cell entry is scheduled (FIFO by due date). Everything downstream flows.
Notes: Pull system. Instead of MRP pushing work to every department, only the cell entry is scheduled, on a visual FIFO board by due date, and one kit is released per pitch. Downstream, FIFO lanes are capped at one drive, so nothing starts until the next station is ready. Upstream, the cell pulls kits from the supermarket, the supermarket triggers machining and fabrication by kanban, and common purchased parts use two-bin kanban. LEI reports Thrustmaster moved from MRP scheduling to visual FIFO scheduling, with finished product pulled by the next operation and WIP easy to see and count.

## Slide 13: FUTURE STATE
Before → Improvement → After: the same people and products, run as a visible flow system.
 | BEFORE | IMPROVEMENT | AFTER
Layout | Functional job shop; ~7 miles walked per unit | P-Q analysis → two size-based assembly cells; defined work areas | Short, one-direction flow; parts at the point of use
Scheduling | MRP / APS push; ~30% schedule attainment | Visual FIFO schedule + 3-day pitch | Predictable cadence; ~80% schedule attainment*
Work method | Tacit and person-dependent | Standard work posted at every station | Repeatable work; faster onboarding
WIP | High, invisible, uncounted | Kits + FIFO lanes capped per station | Low WIP, visible and countable
Quality | ~50% FPY; defects found at test | Built-in checks; stop and fix | FPY target ≥ 90%
Delivery | ~20% on-time delivery | Pull + pitch + daily huddles | 100% on-time delivery within ~18 months*
People | Firefighting and overtime | Cell teams, gemba walks, kaizen | Teams solving problems daily
* Actual results reported by LEI (2016). Other 'After' entries are WG-3 targets.
Notes: Before, improvement, after, row by row. The starred results are what Thrustmaster actually achieved according to LEI: schedule attainment up from about 30% to about 80%, and 100% on-time delivery within about 18 months. The other 'after' entries are our targets.

## Slide 14: KPI DASHBOARD
Eight KPIs to steer the transformation: baselines from the case, targets set by WG-3.
KPI | Before | Target | How we measure it
On-time delivery | ~20% (Q1 2014) | ≥ 95% (Thrustmaster reached 100%) | Orders shipped by promise date ÷ total, weekly
First-pass yield | ~50% (est., Q1 2014) | ≥ 90% | Units passing test first time ÷ units tested
Schedule attainment | ~30% | ≥ 80% | Pitches completed on time ÷ pitches planned
Assembly lead time | Unpredictable; no cadence | 4 pitches (~12 days) per drive in the cell | Kit release → test pass, per drive
WIP | Not visible or counted | ≤ 1 drive per station + 1 per FIFO lane | Count on the pitch board, daily
Walking (motion) | ~7 miles, ~10 h waste per unit | < 1 mile and < 1 h per unit | Spaghetti chart re-study, quarterly
Project cost vs. target | > 100% of target | ≤ 100% (on or under budget) | Actual vs. quoted cost per project
Standard-work coverage | Limited; tacit knowledge | 100% of cell stations | Stations with current, posted standard work
ON-TIME DELIVERY
~20% → ≥ 95%
before → target
FIRST-PASS YIELD
~50% → ≥ 90%
before → target
SCHEDULE ATTAINMENT
~30% → ≥ 80%
before → target
'Before' values: LEI (2016), Q1 2014 baseline where dated. Targets and measures: WG-3.
Notes: We track eight KPIs, more than the five required. Baselines come from the case; targets are ours. The three headline KPIs are on-time delivery, first-pass yield and schedule attainment. For reference, Thrustmaster reached 100% on-time delivery and around 80% schedule attainment. Lead time, WIP and walking turn the flow design into numbers: 4 pitches per drive, WIP capped per station, and under a mile of walking per unit.

## Slide 15: IMPLEMENTATION PLAN
0–30 days → 30–60 days → 60–90 days: pilot one product family, prove it, then extend pull across the shop.
0–30 DAYS See & stabilize
Form the lean team (GM, CI manager, cell leads); train on Lean basics
Map the current-state VSM and a spaghetti chart for tunnel-thruster assembly
P-Q analysis: group drives into size-based families
5S and mark work areas in the pilot zone
Baseline KPIs: OTD, FPY, WIP, walking
MILESTONE
Baseline set; pilot zone 5S'd
30–60 DAYS Build flow
Design the future-state VSM and cell layouts
Move equipment; launch Cell A (small / medium drives)
Write and post standard work for each station
Start the kitting supermarket and 3-day pitch board
Daily 10-minute huddles at the pitch board
MILESTONE
Cell A running to a 3-day pitch
60–90 DAYS Pull & sustain
Launch Cell B (large drives, crane bay)
FIFO lanes + kanban from machining and fabrication
Replace MRP dispatch with a visual FIFO schedule
Built-in quality checks at every station
Leader standard work, gemba walks, monthly KPI review (PDCA)
MILESTONE
Both cells on pull; KPI dashboard live
Notes: A 90-day plan. Days 0–30: see and stabilize. Form the team, map the value stream, run P-Q analysis, 5S the pilot zone and set baselines. Days 30–60: build flow. Launch Cell A with standard work, kitting and the 3-day pitch board, and start daily huddles. Days 60–90: pull and sustain. Launch Cell B, connect upstream with FIFO and kanban, retire MRP dispatching for assembly, add quality gates, and lock in leader standard work and monthly PDCA reviews.

## Slide 16: EXPECTED BUSINESS BENEFITS
Cost ↓ · Quality ↑ · Lead time ↓ · Productivity ↑ · Customer satisfaction ↑
COST ↓
Less overtime, rework and WIP carrying cost; projects back within target and margins widen
QUALITY ↑
Built-in checks and standard work raise first-pass yield from ~50% toward ≥ 90%
LEAD TIME ↓
A fixed 3-day cadence and low WIP make completion dates predictable
PRODUCTIVITY ↑
Walking and searching (~10 h of waste per unit) removed; labour needs visible per cell
CUSTOMER SATISFACTION ↑
Reliable promise dates for shipyards; on-time delivery from ~20% toward 100%
WHAT THRUSTMASTER ACTUALLY ACHIEVED
100%
on-time delivery within ~18 months (from ~20%)
30% → 80%
schedule attainment
Lower cost
significant cost reductions and wider profit margins
Source: LEI, "Thrustmaster Comes Around" (2016); LEI Summit 2016 deck.
Notes: Expected benefits on the five dimensions. On the right is the evidence that this is realistic: LEI reports that within about 18 months Thrustmaster reached 100% on-time delivery, improved schedule attainment from about 30% to about 80%, and achieved significant cost reductions and wider margins.

## Slide 17: DISCUSSION: CAN LEAN WORK IN A HIGH-VARIETY, LOW-VOLUME ENVIRONMENT?
Our answer: yes, if you adapt the tools and standardize the process, not the product.
THE OBJECTION
HOW THRUSTMASTER ANSWERED IT
"Every order is different."
Build steps are roughly the same; group products by size into families. The router carries the specs.
"Takt time is meaningless at low volume."
Use a pitch as the heartbeat: one drive every 3 days.
"Kanban needs repetitive demand."
FIFO lanes and kits for custom parts; kanban only for common parts.
"Standard work kills flexibility."
Standard steps free experts for the truly unique work; cross-trained cell teams flex.
"Better software will fix scheduling."
ERP and APS didn't. Visual flow did: on-time delivery went from ~20% to 100% in ~18 months.
VERDICT: YES, IF ADAPTED. Lean principles (value, flow, pull, standard work, built-in quality) are universal; the tools must fit the product. High-mix shops often gain the most, because their waste (queues, searching, rework) is largest.
Notes: Discussion question. Our position: yes, Lean works in high-variety, low-volume settings, provided you adapt the tools. Take the five common objections in turn and show how Thrustmaster answered each: product families by size, a pitch instead of a seconds-level takt, FIFO and kits instead of pure kanban, standard steps with variable specs, and visual flow instead of more software. Invite the class to challenge where the limits are, for example one-off prototypes or very long engineering cycles.

## Slide 18: KEY LEARNING
Three lessons from Thrustmaster's transformation.
01
Make the work visible before you try to improve it
A value-stream map and a simple spaghetti chart revealed ~7 miles of walking per unit that no report showed.
02
Flow beats software
ERP, an APS system and new machines didn't lift on-time delivery. Cells, pitch, pull and standard work did.
03
Lean fits high-mix, low-volume work
Standardize the process (steps, cadence, work areas), not the product. Variety stays; chaos goes.
Notes: Three key learnings. First, make the work visible: the spaghetti chart showed waste no report captured. Second, flow beats software: the IT fixes failed and the physical and managerial redesign worked. Third, Lean fits high-mix, low-volume work when you standardize the process rather than the product.

## Slide 19: KEY LEARNING
What can other organizations learn from this case?
Start small, at the gemba
Pilot one product family and prove results fast.
AT THRUSTMASTER
The spaghetti chart targeted tunnel-thruster assembly
Segment by product characteristics
Size-based families make flow possible without giving up variety.
AT THRUSTMASTER
Two assembly-cell configurations by product size
Turn tacit knowledge into standard work
It protects quality and speeds onboarding while the workforce grows.
AT THRUSTMASTER
Standard work posted and visible in each work area
Find your heartbeat
When takt is long, use a pitch to create rhythm and catch problems early.
AT THRUSTMASTER
A three-day production pitch
Prefer simple pull to complex scheduling
FIFO lanes, kits and a visual board beat sophisticated software.
AT THRUSTMASTER
Visual FIFO scheduling replaced MRP scheduling
Leaders own the system
A dedicated team and daily leader routines sustain the gains.
AT THRUSTMASTER
The GM and CI manager led the lean team; 100% OTD in ~18 months
Notes: Transferable lessons for any organization: start with a pilot at the gemba; segment work by product characteristics; capture tacit knowledge as standard work; create a heartbeat with pitch when takt is long; prefer simple visual pull to complex scheduling; and make leaders own the system so the gains last.

## Slide 20: REFERENCES
Lean Enterprise Institute (2016). "Thrustmaster Comes Around." The Lean Post. lean.org/the-lean-post/articles/thrustmaster-comes-around
Lean Enterprise Institute (2016). "Propelling Ahead: Thrustmaster of Texas' Lean Journey." Lean Transformation Summit. lean.org/wp-content/uploads/2022/04/LS_Thrustmaster_summit16.pdf
Lean Enterprise Institute. "Small Chart, Big Impact: How a Simple Spaghetti Chart Led to Huge Wins at Thrustmaster of Texas." The Lean Post.
DLW Partners. "Thrustmaster of Texas Story." dlw-partners.com/thrustmaster-of-texas-story
Rother, M. & Shook, J. (1999). Learning to See. Lean Enterprise Institute.
Womack, J. P. & Jones, D. T. (2003). Lean Thinking (2nd ed.). Free Press.
Course brief: Case Study 3, Thrustmaster (Working Group-3), Business Operations Excellence.
Note: figures labelled 'target' or 'illustrative' are WG-3 assumptions, not reported case data.
Thank you
Questions and discussion
Working Group-3 | Section O1
Arpit Shukla · Yash Vardhan Chauhan · Tasleen Kaur · Naman Khatri · Manu R · Abhinav Dongre
Notes: Sources used for case facts and figures. Anything marked as a target or illustrative is our own assumption. Thank the audience and open for questions.