## Slide 1: From 10 to 12 Excavators a Day
BUSINESS OPERATIONS EXCELLENCE · GROUP 3
Applying Operations Excellence to the machine shop at Volvo CE India, Peenya, Bengaluru
Industrial visit: 8 September 2026
Presentation: 3–4 November 2026 · BBA, Group 3
Peenya Industrial Area, Bengaluru
Notes: Good morning. We are Group 3. Our brief from the Volvo CE India visit on 8 September: raise machine-shop output by 20%, from 10 to 12 excavators per 8-hour shift, without hurting quality. Structure: (1) Volvo CE worldwide, (2) the global product segments by application and tonnage, (3) Volvo CE India's Peenya operations and offering, (4) our Group 3 problem: diagnosis, six Operations Excellence levers, results and a 12-week roadmap. Note: machine-shop cycle times and losses are assumed figures for analysis, as the brief allows.

## Slide 2: Volvo CE worldwide at a glance
1 · VOLVO CE WORLDWIDE
SEK 81.6 bn
Net sales 2025 (≈ ₹ 74,000 cr)
13.3%
Adjusted operating margin 2025
~13,000
Employees, 85 nationalities
180
Markets served via dealers
Brands
VOLVO · premium machines
ROKBAK · haulers, Scotland
SDLG stake (70%) sold in Sep 2025; dealer Swecon bought in Jan 2026
Chart: 2025 net sales by region, SEK bn (Volvo CE Q4 2025 report)
| Europe | Asia | North America | Rest of world
Net sales 2025 | 27.8 | 23.4 | 19.3 | 11.2
Plants in Sweden, Germany, France, Poland, UK, USA, Brazil, South Korea, China and India
1832
Munktell starts the business in Eskilstuna, Sweden
1950
Volvo buys Bolinder-Munktell
1995
Renamed Volvo Construction Equipment
1997
Volvo CE India starts in Bengaluru
2025
Exits SDLG; new Eskilstuna excavator plant
2026
Buys Swecon; EC650 launched in India
Notes: Volvo CE traces its roots to 1832, when Johan Theofron Munktell began making machines in Eskilstuna, Sweden, which makes it one of the oldest industrial companies still building construction equipment. Volvo bought Bolinder-Munktell in 1950, and the business became Volvo BM in 1973 and Volvo Construction Equipment in 1995. It is a business area of the Volvo Group (about 99,000 employees and SEK 479 bn sales in 2025). 2025: net sales SEK 81.6 bn (2024: SEK 88.3 bn), adjusted operating margin 13.3%. By region: Europe 27.8, Asia 23.4, North America 19.3, rest of world (South America, Africa and Oceania) about 11.2 SEK bn. About 13,000 employees of 85 nationalities (Jan 2026). Brands: Volvo (premium) and Rokbak (articulated haulers, Motherwell, Scotland). Volvo CE sold its 70% stake in China's SDLG to Lingong Group for SEK 8 bn (closed 1 Sep 2025) and bought its largest European dealer, Swecon, for SEK 7 bn (Jan 2026). A new crawler excavator plant (up to 3,500 machines a year, 14–50 t) is planned at Eskilstuna. Sources: Volvo CE Q4 2025 report; volvoce.com company information; Volvo Group press releases (Jun/Sep 2025, Nov 2025, Jan 2026). SEK to INR conversion is approximate.

## Slide 3: Global portfolio: application & tonnage
2 · PRODUCT SEGMENTS BY APPLICATION AND TONNAGE
Product line
Main applications
0
25
50
75
100 t
Compact excavators
ECR18 → ECR88
1.5–9 t
Utilities, landscaping, urban sites, rental
Wheeled excavators
EW60 → EW240
6–24 t
Urban roadworks, utilities, material handling
Crawler excavators
EC140 → EC950
14–95 t
Infrastructure, quarrying, mining
Compact wheel loaders
L20 → L50
4.5–10 t
Landscaping, agriculture, rental
Wheel loaders
L60 → L350
11–56 t
Aggregates, recycling, ports, forestry
Articulated haulers
A25 → A60 · Rokbak RA30/40
24–55 t payload
Earthmoving, quarrying, mining
Road machinery
Compactors · ABG pavers
≈1.5–22 t
Road building, highways, airports
Electric models offered (e.g., ECR25, EC230, L25, L120 Electric). Bars show approx. operating weight; haulers show rated payload (Volvo CE spec sheets).
Notes: Volvo CE segments its machines by application and size. Excavators: compact (about 1.5–9 t) for utilities and urban work; wheeled (6–24 t) for roadworks and material handling; crawler (14–95 t, EC140 to EC950) for infrastructure, quarrying and mining. Loaders: compact wheel loaders (L20–L50) for landscaping, agriculture and rental; wheel loaders L60 to L350 (11–56 t) for aggregates, recycling, ports and forestry. Haulers: Volvo articulated haulers A25 to A60 carry 24–55 t; Rokbak RA30/RA40 serve the value segment. Road machinery: soil and asphalt compactors and ABG pavers for road building. Electromobility: Volvo offers electric compact excavators and loaders plus the EC230 Electric and L120 Electric. Figures are approximate operating weights from Volvo CE regional spec pages (e.g., EC950 about 91–95 t, L350H about 50–56 t).

## Slide 4: Volvo CE India: the Peenya hub
3 · VOLVO CE INDIA OPERATIONS
Where
India HQ and plant in Peenya Industrial Area, Bengaluru
History
Site since 1978; Volvo CE India since 1997; ₹90 cr upgrade and new excavator line in 2011
What it builds
Crawler excavators, soil compactors and asphalt pavers; EC210 is ~70% localised
Market reach
19 dealers, 180+ touchpoints; ~6.5% Indian CE share (2024); exports to emerging markets
Engineering
Bengaluru Technology Centre: R&D and localisation for India and the world
From steel to machine at Peenya
1 Receiving
Steel plate, castings, purchased parts
2 Fabrication
Cutting and welding of booms, arms, frames
3 Machine shop
Boring, milling, drilling: our focus
4 Paint shop
Frames primed and painted
5 Assembly
Line paced by the digital takt board
6 Test & dispatch
Function test, final inspection, dispatch
Recent milestones
Dec 2025 · EXCON, Bengaluru
EC215 “Made in Bharat” 20–22 t excavator unveiled
Sep 2026 · bauma CONEXPO INDIA
EC650, a 65 t mining excavator, launched
2027 · Next
Localised medium wheel loaders after SDLG exit
Notes: Volvo CE India Pvt. Ltd. has its India headquarters and plant in the Peenya Industrial Area, Bengaluru. The site dates to 1978 and Volvo CE has operated in India since 1997. In 2011 Volvo CE invested SEK 144 million (about ₹90 crore) to upgrade the plant and opened a new excavator assembly line; the first EC210B Prime and EC290B rolled off it. The plant specialises in crawler excavators, soil compactors and asphalt pavers. The EC210 is about 70% localised and Peenya also exports to selected emerging markets. Process flow we saw: receiving → fabrication (welding of booms, arms, upper and lower frames) → machine shop (boring of pin bores, milling the swing-bearing face, drilling and tapping) → paint shop → assembly line paced by the digital takt board → function test, final inspection and dispatch. Group 3's focus is step 3, the machine shop. Network: 19 dealers, 800+ dealer staff, 180+ touchpoints. MD Dimitrov Krishnan cited about 6.5% share of the Indian CE market (2024). Milestones: EXCON 2025 in Bengaluru (EC215, SD110, L120 Electric); bauma CONEXPO INDIA, Sep 2026 (EC650); localised medium wheel loaders are planned for 2027 from the Bengaluru Technology Centre. Sources: volvoce.com Bangalore location page; Volvo CE press release 2011; Autocar Professional, The Machine Maker, ANI (2024–2026).

## Slide 5: India offering: application & tonnage
3 · VOLVO CE INDIA PRODUCT OFFERING
Segment | Models | Tonnage | Typical applications in India
20–22 t crawler excavators | EC210, EC215, EC220 ● Built at Peenya | 20–22 t | Highways, irrigation canals, urban infra, stone quarries
Heavy crawler excavators | EC300, EC380, EC480 | 30–48 t | Quarrying, mass earthmoving, overburden removal
Mining excavators | EC650 (new, Sep 2026), EC750 | 65–75 t | Coal and iron-ore mines
Wheel loaders | Premium L-series incl. L120 Electric | ≈20 t + | Mining, cement, steel plants, ports (~100 a year)
Soil compactors | SD110 / SD110C ● Built at Peenya | ≈11 t | Highway embankments, sub-grade compaction
Asphalt compactors | DD90C, DD100C, PT220 | ≈9–10 t | Bituminous surfacing of roads
Asphalt pavers (ABG) | P4370D wheeled; P5320D–P8820D tracked ● Built at Peenya | Paving width | National highways and expressways
WHY +20% MATTERS
≈70%
of India's 30,000–35,000 excavators a year are in the 20 t class, the core of the Peenya line
4% → 8%+
Volvo CE India's 20 t share in 2024 and its goal to more than double it
More demand at Peenya means the machine shop must deliver more units per shift.
Notes: Volvo CE India covers four application clusters: (1) construction and infrastructure with 20–22 t excavators (EC210, the India-built EC215 'Made in Bharat' and EC220), where the 20 t class is about 70% of India's 30,000–35,000 excavators a year; (2) quarrying and heavy earthmoving with 30–48 t excavators; (3) mining with the 65 t EC650 launched at bauma CONEXPO INDIA in September 2026 and the 75 t EC750; (4) road building with SD110 soil compactors, DD90C/DD100C double-drum and PT220 pneumatic compactors, and ABG pavers (P4370D wheeled, P5320D–P8820D tracked). Wheel loaders: about 100 premium Volvo units a year for mining and industry; after the SDLG exit, localised medium wheel loaders are planned for 2027. Some machines use Volvo-Eicher CV5 engines. Link to our problem: Volvo CE India held about 4% of the 20 t excavator segment in 2024 and aims to more than double it. Growth on that scale needs more output from Peenya, which is our brief. Sources: volvoce.com/en-in product pages; Autocar Professional (Jun 2024, Dec 2025, Sep 2026); The Machine Maker; NBM&CW.

## Slide 6: The brief: 10 → 12 excavators a shift
4 · GROUP 3 PROBLEM STATEMENT
10
excavators per 8-hour shift today (assumed)
12
target per shift: +20%, i.e. 2 more units
420
minutes available per shift after breaks
42 → 35
takt time, minutes per excavator
Where the 420 minutes come from
480
shift
−
30
lunch
−
20
2 tea breaks
−
10
start-up & 5S
=
420
available
Takt = available time ÷ demand
420 ÷ 10 = 42 min today → 420 ÷ 12 = 35 min target
Ground rules we set ourselves
Same 8-hour shift and the same headcount
No compromise on quality (first-pass yield, Cpk) or safety
Minimal capex: fix the process before buying capacity
Scope: machine shop feeding the EC210/215/220 line
Overtime or a 2nd shift
Adds cost; fatigue raises the quality risk
Buy another machining centre
₹4–5 cr capex and a 9–12 month wait
Operations Excellence ✓
Low capex, ~12 weeks, builds lasting capability
Notes: The brief: 10 excavators per 8-hour shift today (assumed, as allowed). The production manager must reach 12 a day, which is +20% or two more machines, without hurting quality. The brief's wording 'current production rate, which is 12' is read as 10 today and 12 as the target. Available time: 480 min shift minus 30 lunch, 2 x 10 tea breaks and a 10-minute start-up meeting with 5S leaves 420 min. Takt time = available time / customer demand: 420/10 = 42 min today, 420/12 = 35 min target. Every machine-shop operation must therefore finish one excavator's parts in 35 minutes or less. Options: overtime or a second shift adds cost, and fatigue is a quality risk. A new 5-axis machining centre is roughly ₹4–5 crore (indicative) with a 9–12 month lead time. Operations Excellence attacks waste with low capex in about 12 weeks and builds capability, so we choose it.

## Slide 7: Gemba finding: OP30 sets the pace
4 · CURRENT STATE OF THE MACHINE SHOP
Chart: Effective cycle time per operation, min per excavator (assumed data)
| OP10 Boom | OP20 Arm | OP30 Upper frame | OP40 Lower frame | OP50 Links & pins | OP60 Wash & CMM
Effective cycle time | 39 | 36 | 0 | 38 | 27 | 30
Bottleneck (OP30) | 0 | 0 | 42 | 0 | 0 | 0
Takt today (42 min) | 42 | 42 | 42 | 42 | 42 | 42
Target takt (35 min) | 35 | 35 | 35 | 35 | 35 | 35
Gemba findings (assumed)
1
OP30 (upper frame, 5-face machining centre) runs at 42 min = takt: zero spare capacity
2
4 of 6 operations are slower than the 35 min target takt
3
Frames wait for the shared overhead crane and first-off QC sign-off
4
Manual dial-gauge alignment and 3 model changeovers a day (EC210/215/220)
Notes: Assumed routing for one excavator's structural parts after welding: OP10 boom and OP20 arm on horizontal boring mills (pin bores); OP30 upper (revolving) frame on a 5-face machining centre (swing-bearing face, boom-foot bores, drilling and tapping); OP40 lower frame and track frames; OP50 links, pins and small parts on a VMC; OP60 deburr, wash and CMM check, then the paint shop. Effective cycle time includes each station's losses. OP30 needs 42 min, which equals today's takt, so it is the bottleneck (Theory of Constraints, step 1: identify the constraint). At the 35-min target takt, OP10, OP20, OP30 and OP40 are all too slow; OP50 and OP60 have spare capacity. Findings assumed for the analysis (replace with what your group actually observed if different): frames wait for the shared EOT crane and first-off quality sign-off; set-up uses a dial gauge; three model changeovers a day between EC210/215/220 frames.

## Slide 8: Where OP30's 420 minutes go today
4 · LOSS ANALYSIS AT THE BOTTLENECK (OEE)
Chart: 
| Value-adding machining | Changeovers | Breakdowns & minor stops | Waiting: crane, parts, QC | Slow set-up: dial-gauge alignment | Rework / re-machining
OP30 minutes | 300 | 45 | 25 | 20 | 15 | 15
420
minutes
Value-adding machining 300 min
10 good frames × 30 min each
Changeovers 45 min
Availability loss
Breakdowns & minor stops 25 min
Availability loss
Waiting: crane, parts, QC 20 min
Performance loss
Slow set-up: dial-gauge alignment 15 min
Performance loss
Rework / re-machining 15 min
Quality loss
Availability
(420 − 45 − 25) ÷ 420
83.3%
Performance
28-min ideal × 10.5 frames ÷ 350 min
84.0%
Quality
10 good ÷ 10.5 frames machined
95.2%
OEE = A × P × Q
World-class benchmark ≈ 85%
66.7%
120 lost minutes a day = 4 excavators' worth of OP30 time. Win back about 60 of them and the shop makes 2 more machines with no new machine and no rushing.
Notes: We split OP30's 420 available minutes into Nakajima's six big losses. Only 300 minutes add value. Changeovers take 45 (3 x 15), breakdowns and minor stops 25, waiting for the crane, parts or QC 20, slow dial-gauge set-up 15, and rework 15. OEE = Availability x Performance x Quality. A = (420 − 70)/420 = 83.3%. P = (28-min ideal cycle x 10.5 frames)/350 run minutes = 84.0%. Q = 10 good / 10.5 machined = 95.2%. OEE = 66.7%, against a world-class benchmark of about 85%. Check: 10 good x 28 / 420 = 66.7%. Key insight: the 120 lost minutes equal four excavators' worth of OP30 machining at 30 min each. We only need about 60 of them back to make 2 more machines. The extra output comes from removing waste, not from operators working faster.

## Slide 9: Levers 1–3: stabilise and feed OP30
5 · SOLUTION: PROCESS STABILITY AND JUST-IN-TIME
Theory of Constraints: fix the bottleneck (OP30) first, because a minute saved there is a minute of plant output; then roll out to OP10, OP20 and OP40.
VPS · PROCESS STABILITY
1 · SMED quick changeover
45 → 15 min/day
+1.0 excavator of capacity
Preset the next frame's fixture and tools while the current frame is machined
Zero-point quick clamps and a tool presetter: 15 → 5 min per change
Sequence frames by family (EC210/215/220)
KPI minutes per changeover (goal ≤ 5)
VPS · PROCESS STABILITY
2 · TPM for the machines
25 → 12 min/day
+0.4 excavator of capacity
Operators do a 10-min daily clean-lubricate-inspect-tighten check
Planned maintenance calendar and spindle vibration monitoring
Critical spares kit at the machine to cut repair time
KPI MTBF up, MTTR down, breakdown min/shift
VPS · JUST-IN-TIME
3 · JIT flow and kitting
20 → 6 min/day
+0.5 excavator of capacity
FIFO lane with a 2-frame buffer so OP30 is never starved
Kanban pull of weldments from fabrication; tool kits per model
Dedicated jib crane at OP30: no waiting for the shared crane
KPI minutes OP30 waits for a frame (goal ≤ 6)
Notes: We frame the levers with the Volvo Production System (VPS): teamwork as the foundation; process stability, built-in quality and just-in-time as pillars; continuous improvement on top. We apply Theory of Constraints first: exploit OP30, subordinate the other stations to it, then roll the gains out. Lever 1, SMED: split internal from external set-up. The next model's fixture and tools are preset offline while the current frame is cut. Zero-point quick clamps and a tool presetter cut each changeover from 15 to 5 min, so 45 → 15 min a day. Frames are sequenced by family. Gain: 30 min, about 1.0 excavator of capacity at a 29-min cycle. Lever 2, TPM: autonomous maintenance by operators (a daily CLIT check: clean, lubricate, inspect, tighten), a planned-maintenance calendar, spindle vibration and coolant monitoring, and a spares kit to cut MTTR. Breakdowns 25 → 12 min/day: +0.4 unit. Lever 3, JIT: a FIFO lane with a 2-frame buffer in front of OP30 (the TOC 'buffer'), Kanban pull of weldments from fabrication, model-wise tool kits and a dedicated jib crane. Waiting 20 → 6 min/day: +0.5 unit.

## Slide 10: Levers 4–6: standardise, protect quality
5 · SOLUTION: STANDARD WORK, BUILT-IN QUALITY, KAIZEN
Chart: Line balancing: effective cycle time, min per excavator
| OP10 Boom | OP20 Arm | OP30 Upper frame | OP40 Lower frame | OP50 Links & pins | OP60 Wash & CMM
Before | 39 | 36 | 42 | 38 | 27 | 30
After | 33 | 31 | 32.5 | 33 | 30 | 28
Target takt (35 min) | 35 | 35 | 35 | 35 | 35 | 35
4 · Standard work & line balancing
Slow set-up 15 → 6 min; cycle 30 → 29 min · +0.7 excavator
Time-study standard work; drilling moved from OP10/40 to OP50
Probing replaces dial-gauge set-up; CNC paths optimised
5 · Built-in quality: poka-yoke, SPC, jidoka
Rework 15 → 6 min · +0.3 excavator
Poka-yoke locators: a frame cannot be clamped the wrong way
SPC on pin bores (Cpk ≥ 1.33); machine stops on tool wear
6 · 5S, visual management & kaizen
Sustains the gains shift after shift
5S, shadow boards; hourly output and OEE on the digital board
Daily tier meetings, PDCA kaizen, operator skill matrix
Notes: Lever 4, standardised work and line balancing: a time study gives each operation a standard work chart. Using a Yamazumi view we move non-critical drilling and tapping from OP10 and OP40 to the VMC at OP50, which had spare time (OP50 rises 27 → 30 min but stays under takt). In-machine probing (e.g., Renishaw-type) replaces dial-gauge alignment, and CNC tool paths are optimised within validated feeds and speeds. Slow set-up 15 → 6 min and cycle 30 → 29 min: +0.7 unit. Lever 5, built-in quality: poka-yoke locating pins make wrong clamping impossible; the probe checks critical pin bores before the frame is unloaded; SPC charts on bores with Cpk ≥ 1.33; jidoka, so the machine stops itself on a tool-wear or out-of-tolerance alarm. Rework 15 → 6 min: +0.3 unit, and fewer defects reach paint and assembly. Lever 6, 5S, visual management and kaizen: 5S and shadow boards at every machine; hour-by-hour output, OEE and Andon on the digital board; daily tier-1/tier-2 meetings; PDCA kaizen; a skill matrix so operators can cover breaks. This sustains the other five levers. Result in the chart: every operation is at or below the 35-min target takt.

## Slide 11: Result: capacity for 12.9, plan for 12
6 · IMPACT
OP30 capacity bridge, excavators per shift
8
9
10
11
12
13
10.0
Today
+1.0
SMED
+0.4
TPM
+0.5
JIT flow
+0.7
Standard
work
+0.3
Built-in
quality
12.9
After
Target 12
Axis starts at 8 so the increments are visible. Values use the assumed data model.
KPI | Today | After 12 weeks
Output, excavators per shift | 10 | 12 (capacity 12.9)
OEE at OP30 | 66.7% | 86% capability
Effective cycle time at OP30 | 42 min | 32.5 min
Changeover per model | 15 min | 5 min
Breakdown loss per shift | 25 min | 12 min
First-pass yield at OP30 | 95.2% | 98.4%
Robust: even if only 70% of the gains hold, capacity is 12.05, still above target.
Upside not counted: relief operator runs OP30 through tea breaks (+20 min ≈ +0.7 unit).
Notes: Capacity bridge at OP30, in excavators per shift. Freed minutes are converted at the new 29-min cycle: SMED 30 min (+1.0), TPM 13 min (+0.4), JIT 14 min (+0.5), standard work 9 min of slow set-up plus 10 min from the faster cycle (+0.7), built-in quality 9 min less rework (+0.3). Total 10 → 12.9. Check: losses fall from 120 to 45 min (15 changeover, 12 breakdown, 6 waiting, 6 slow set-up, 6 rework). Good output = (420 − 45)/29 = 12.9 excavators. After-state OEE: A = 393/420 = 93.6%, P = 28 x 13.14/393 = 93.6%, Q = 98.4% → 86% capability. Scheduled at 12 a day, OP30 is loaded to 80% OEE, which keeps about 7% protective capacity. Robustness: at 70% realisation, 10 + 0.7 x 2.93 = 12.05 units. Upside not counted: a multi-skilled relief operator keeps OP30 running through the two tea breaks (+20 min, about +0.7 unit).

## Slide 12: 12-week roadmap to 12 a day
7 · IMPLEMENTATION AND TAKEAWAYS
WEEKS 1–2 · PLAN
Diagnose
Gemba walks, time study
OEE baseline at OP30
Kaizen team formed
Output 10.0 / shift
›
WEEKS 3–6 · DO
Quick wins
5S and visual boards
SMED workshop at OP30
FIFO lane, kits, jib crane
Output 11.0 / shift
›
WEEKS 7–10 · DO
Structural fixes
TPM steps 1–3
Probing, quick clamps, CNC
Poka-yoke; move drilling
Output 11.6 / shift
›
WEEKS 11–12 · CHECK–ACT
Lock in
Verify FPY and Cpk
Freeze standard work
Roll out to OP10/20/40
Output 12.0 / shift
Waste, not speed
Most of the 2 extra machines come from winning back 75 of OP30's 120 lost minutes
Quality by design
No inspection step removed; validated feeds; FPY < 98% or Cpk < 1.33 means stop and fix
VPS sustains it
Standard work, daily tier meetings and kaizen keep OP30 under the 35-min takt
Thank you. Questions welcome.
Notes: Roadmap (PDCA): weeks 1–2 Plan: Gemba walks, time study, OEE baseline and a cross-functional kaizen team (production, maintenance, quality, industrial engineering, operators). Weeks 3–6 Do, quick wins: 5S, visual boards, SMED workshop at OP30, FIFO lane, kitting and jib crane, reaching about 11 a shift. Weeks 7–10 Do, structural: TPM steps 1–3, probing and zero-point clamps, CNC optimisation, poka-yoke, moving drilling to OP50, about 11.6. Weeks 11–12 Check and Act: verify FPY/Cpk, freeze standard work, layered audits, roll out to OP10/20/40, reaching 12. Takeaways: (1) the extra output comes from removing waste: most of it from 75 of 120 lost minutes, the rest from a 1-min faster validated cycle. (2) Quality is protected by design: no inspection step is removed, feeds and speeds stay within validated limits, and FPY or Cpk below target triggers stop-and-fix. (3) The Volvo Production System culture of teamwork, standard work and daily improvement sustains it. Thank you. We welcome your questions.