## Slide 1: From 10 to 12 excavators a day
BUSINESS OPERATIONS EXCELLENCE | GROUP 3
How we would lift output at Volvo CE India's machine shop in Peenya, Bengaluru
Industrial visit: 8 September 2026
Presented 3–4 November 2026 | BBA, Group 3
Notes: Good morning, everyone. We're Group 3. On 8 September we visited Volvo CE India's plant in Peenya, and the production manager left us with a simple-sounding challenge: get the machine shop from 10 to 12 excavators a shift, which is 20% more, without letting quality slip. We'll take it in four parts: who Volvo CE is, what it makes, what the Peenya plant does, and then our problem, our diagnosis and our plan. One honest disclaimer before we start: the machine-shop cycle times and losses are our own assumptions, which the brief allows. The company facts come from Volvo's published reports.

## Slide 2: Volvo CE: big, global and profitable
SEK 81.6 bn
net sales in 2025 (about ₹74,000 crore)
13.3%
adjusted operating margin
~13,000
people, selling in 180 markets
Chart: 2025 net sales by region (SEK bn)
| Europe | Asia | North America | Rest of world
Net sales 2025 | 27.8 | 23.4 | 19.3 | 11.2
1832
Founded in Eskilstuna, Sweden
1950
Bought by Volvo
1997
Arrives in India, in Bengaluru
2025
Exits SDLG to focus on Volvo and Rokbak
Notes: Let's start with the big picture. Volvo CE goes back to 1832, when Johan Theofron Munktell started making machines in Eskilstuna, Sweden. Volvo bought the business in 1950, it took the Volvo Construction Equipment name in 1995, and it came to India in 1997. Today it's a business area of the Volvo Group. In 2025 it sold SEK 81.6 billion worth of machines, roughly ₹74,000 crore. That's a little down from SEK 88.3 billion in 2024, but it still made a 13.3% adjusted operating margin. Europe is the biggest region, followed by Asia and North America. About 13,000 people work there, from 85 nationalities. Two recent moves are worth knowing. In September 2025 it sold its 70% stake in China's SDLG for SEK 8 billion, and in January 2026 it bought Swecon, its largest European dealer, for SEK 7 billion. So the focus is now on two brands: Volvo for premium machines and Rokbak for haulers. Sources: Volvo CE Q4 2025 report, volvoce.com, Volvo Group press releases. The rupee figure is approximate.

## Slide 3: Seven product families, from 1.5 t to 95 t
0
25
50
75
100 t
Compact excavators
Utilities and city sites
1.5–9 t
Wheeled excavators
Roadworks, material handling
6–24 t
Crawler excavators
Infrastructure, quarries, mines
14–95 t
Compact wheel loaders
Landscaping and farms
4.5–10 t
Wheel loaders
Aggregates, ports, recycling
11–56 t
Articulated haulers
Earthmoving and mining
24–55 t payload
Road machinery
Roads, highways, airports
1.5–22 t
Peenya builds these
Bars show approximate operating weight (haulers show payload). Electric versions exist for compact machines, the EC230 and the L120. Source: Volvo CE spec sheets.
Notes: Volvo CE organises its range by application and size. Each bar shows the weight range of one product family. Compact excavators, about 1.5 to 9 tonnes, go to utilities and city sites. Wheeled excavators, 6 to 24 tonnes, handle roadworks. Crawler excavators are the big range, from the 14-tonne EC140 up to the 95-tonne EC950, used for infrastructure, quarries and mines. That's the family Peenya builds, which is why we've highlighted it. Then the loaders: compact wheel loaders L20 to L50 for landscaping and farms, and wheel loaders L60 to L350, 11 to 56 tonnes, for aggregates, ports and recycling. Articulated haulers A25 to A60 carry 24 to 55 tonnes, and the Rokbak RA30 and RA40 cover the value end. Road machinery means soil and asphalt compactors and ABG pavers. Volvo also sells electric versions, for example the ECR25 and L25 compacts, the EC230 Electric and the L120 Electric. Weights are approximate, from Volvo CE spec sheets.

## Slide 4: Peenya is Volvo CE's home in India
Here since 1997
Plant in Peenya Industrial Area, Bengaluru. A new ₹90 crore excavator line opened in 2011.
What it makes
Crawler excavators, soil compactors and asphalt pavers. The EC210 is about 70% made in India.
Who it serves
19 dealers and 180+ touchpoints, about 6.5% of India's market, plus some exports.
How a machine comes together at Peenya
Receiving
Fabrication
Machine shop
Paint shop
Assembly
Test & dispatch
Our focus: boring, milling and drilling the booms, arms and frames that come out of fabrication
Notes: Now to India. Volvo CE India's headquarters and plant sit in the Peenya Industrial Area in Bengaluru. The site goes back to 1978, and Volvo CE has been in India since 1997. In 2011 it invested SEK 144 million, about ₹90 crore, in an upgrade and a new excavator assembly line. Peenya builds crawler excavators, soil compactors and asphalt pavers. The EC210 is about 70% localised, and some machines are exported to other emerging markets. Through 19 dealers, 800+ dealer staff and 180+ touchpoints, Volvo has roughly 6.5% of the Indian construction equipment market, according to the MD in 2024. At the bottom is the flow we saw on our visit. Steel and parts come in, fabrication welds the booms, arms and frames, the machine shop bores, mills and drills them, then paint, then assembly on a line paced by a digital takt board, and finally testing and dispatch. Our project is step three, the machine shop. A few milestones: the EC215 'Made in Bharat' excavator was unveiled at EXCON in December 2025, the 65-tonne EC650 launched at bauma CONEXPO INDIA in September 2026, and locally built medium wheel loaders are planned for 2027 from the Bengaluru Technology Centre. Sources: volvoce.com, Volvo CE 2011 press release, Autocar Professional, The Machine Maker, ANI.

## Slide 5: In India, the 20-tonne excavator is king
≈70%
of the 30,000–35,000 excavators sold in India each year are in the 20 t class
4% → 8%+
Volvo's share of that class in 2024, and where it wants to be
What Volvo CE sells in India
Used for | Models | Weight
Construction and infrastructure | EC210, EC215, EC220 (built at Peenya) | 20–22 t
Quarrying and earthmoving | EC300, EC380, EC480 | 30–48 t
Mining | EC650 (new in 2026), EC750 | 65–75 t
Road building | Compactors and ABG pavers (built at Peenya) | about 9–11 t
More 20 t machines sold means Peenya's machine shop has to make more every shift. That's where our project comes in.
Notes: Why does any of this matter for our problem? Because of this number. About 70% of the 30,000 to 35,000 excavators sold in India every year are in the 20-tonne class, and that's exactly what Peenya's line makes. In 2024 Volvo held about 4% of that segment, and it wants to more than double it. On the right is the India range. The 20 to 22-tonne EC210, EC215 and EC220 go to highways, irrigation canals, city projects and stone quarries. Heavier 30 to 48-tonne machines handle quarrying and overburden removal. The EC650 and EC750 serve coal and iron-ore mines. For roads there are SD110 soil compactors, DD90C and DD100C double-drum and PT220 pneumatic compactors, and ABG pavers. Volvo also sells around 100 premium wheel loaders a year here, including the L120 Electric. So if Volvo wins more of the 20-tonne market, Peenya has to build more machines. And that brings us to our brief. Sources: volvoce.com/en-in, Autocar Professional, The Machine Maker, NBM&CW.

## Slide 6: The ask: two more excavators every shift
10 → 12
excavators per 8-hour shift, today vs target (+20%)
42 → 35 min
takt time: 420 working minutes shared across the excavators we need
Our ground rules
Same shift, same team
No compromise on quality or safety
Fix the process before buying machines
Three ways to get there
Overtime or a second shift
Costs more, and tired people make more mistakes
Buy another machining centre
₹4–5 crore, and a 9–12 month wait for delivery
Operations Excellence
Low cost, about 12 weeks, and the skills stay with the plant
OUR PICK
Notes: Here's the brief. Today the machine shop supports 10 excavators per 8-hour shift. We assumed that figure, as the brief allowed. The target is 12, which is two more machines, or 20%. Where does takt time come from? An 8-hour shift is 480 minutes. Take off 30 for lunch, two 10-minute tea breaks and a 10-minute start-up and 5S meeting, and you're left with 420 working minutes. Takt is available time divided by demand: 420 divided by 10 gives 42 minutes per excavator today. For 12, it drops to 35 minutes. So every machine-shop step has to finish one excavator's parts in 35 minutes or less. We set ourselves some rules: same shift and same headcount, no compromise on quality or safety, and fix the process before spending on new capacity. Our scope is the machine shop feeding the EC210, 215 and 220 line. We looked at three options. Overtime or a second shift costs more, and fatigue raises the risk of mistakes. A new 5-axis machining centre costs around ₹4 to 5 crore and takes 9 to 12 months to arrive. Operations Excellence is cheap, takes about 12 weeks and builds skills that stay with the plant. So that's what we chose.

## Slide 7: One machine, OP30, sets the pace
Chart: Minutes per excavator at each step (assumed data)
| OP10 Boom | OP20 Arm | OP30 Upper frame | OP40 Lower frame | OP50 Links & pins | OP60 Wash & CMM
Other steps | 39 | 36 | 0 | 38 | 27 | 30
OP30, the bottleneck | 0 | 0 | 42 | 0 | 0 | 0
Target takt (35 min) | 35 | 35 | 35 | 35 | 35 | 35
What we saw on the shop floor
1
OP30 needs 42 min per frame, exactly today's takt. There's no slack at all.
2
4 of the 6 steps are slower than the 35 min we'll need.
3
Frames sit waiting for the shared crane and for QC sign-off.
4
Set-up is done by hand with a dial gauge, with 3 model changes a day.
Notes: Next we did a Gemba walk, which simply means going to where the work happens and watching. After welding, each excavator's structural parts go through six machining steps: the boom and arm on horizontal boring mills, the upper frame on a 5-face machining centre at OP30, the lower and track frames at OP40, links and pins on a vertical machining centre at OP50, then deburring, washing and a CMM check at OP60 before paint. The chart shows how long each step really takes per excavator, including its losses. OP30 needs 42 minutes, exactly today's takt. That makes it the bottleneck, or in Theory of Constraints language, the step that sets the pace for the whole shop. Against the new 35-minute target, four of the six steps are too slow. OP50 and OP60 have spare time. What's slowing things down? Frames wait for the shared overhead crane and for first-off quality sign-off, set-up is done by hand with a dial gauge, and there are three model changeovers a day between EC210, EC215 and EC220 frames. These findings are assumed for our analysis.

## Slide 8: Only 300 of OP30's 420 minutes make parts
Chart: 
| Making parts | Changeovers | Breakdowns and small stops | Waiting for crane, parts, QC | Slow set-up (dial gauge) | Rework
OP30 minutes | 300 | 45 | 25 | 20 | 15 | 15
420
minutes a day
Making parts
300 min
Changeovers
45 min
Breakdowns and small stops
25 min
Waiting for crane, parts, QC
20 min
Slow set-up (dial gauge)
15 min
Rework
15 min
OEE at OP30 today
66.7%
World class is about 85%
Availability 83% × Performance 84% × Quality 95%
We lose 120 minutes a day, which is 4 excavators' worth of OP30 time. Win back about half and we get our 2 extra machines, without anyone working faster.
Notes: So where do OP30's 420 minutes actually go? Only 300 minutes are spent making parts: 10 good frames at 30 minutes each. The rest is lost to what Nakajima called the six big losses: 45 minutes on changeovers, three a day at 15 minutes each; 25 on breakdowns and small stops; 20 waiting for the crane, parts or QC; 15 on slow dial-gauge set-up; and 15 on rework. That gives an OEE of 66.7%. The working: availability is 420 minus 70, over 420, so 83.3%. Performance is a 28-minute ideal cycle times 10.5 frames, over 350 running minutes, so 84%. Quality is 10 good frames out of 10.5 machined, so 95.2%. Multiply them and you get 66.7%. As a check, 10 good frames times 28 minutes, over 420, is also 66.7%. World class is around 85%. Here's the key insight. 120 lost minutes is four excavators' worth of OP30 time at 30 minutes each. We only need about 60 of them back to make two more machines. The extra output comes from removing waste, not from people working faster.

## Slide 9: First, keep OP30 running
A minute saved at the bottleneck is a minute saved for the whole plant. So we start at OP30, then roll out to the other steps.
SMED
Quicker changeovers
45 → 15
minutes a day on changeovers
Prepare the next fixture while the current frame is still being cut, and use quick-release clamps.
+1.0 excavator a shift
TPM
Fewer breakdowns
25 → 12
minutes a day lost to stops
Operators do a 10-minute daily check, backed by a planned maintenance calendar.
+0.4 excavator a shift
JUST-IN-TIME
No more waiting
20 → 6
minutes a day spent waiting
A two-frame buffer in front of OP30, kanban from welding, and its own jib crane.
+0.5 excavator a shift
Notes: Our solution is built on the Volvo Production System: teamwork at the base, then process stability, built-in quality and just-in-time as the pillars, and continuous improvement on top. We start at OP30 because of Theory of Constraints: a minute saved at the bottleneck is a minute saved for the whole plant. Then we roll the ideas out to OP10, OP20 and OP40. Lever 1 is SMED, or quick changeover. We separate what has to happen with the machine stopped from what can happen while it runs, so the next model's fixture and tools are preset offline. Zero-point quick clamps and a tool presetter cut each changeover from 15 to 5 minutes, so 45 minutes a day becomes 15. Sequencing frames by model family helps too. That's worth about one extra excavator. We'd track minutes per changeover, with a goal of 5 or less. Lever 2 is TPM. Operators do a 10-minute daily clean, lubricate, inspect and tighten check. Add a planned maintenance calendar, spindle vibration monitoring and a critical spares kit at the machine. Breakdowns go from 25 to 12 minutes a day, which is about 0.4 of an excavator. We'd track MTBF, MTTR and breakdown minutes per shift. Lever 3 is just-in-time flow. A first-in, first-out lane with a two-frame buffer means OP30 never runs out of work. Weldments are pulled from fabrication with kanban, tools are kitted per model, and OP30 gets its own jib crane so it doesn't wait for the shared one. Waiting goes from 20 to 6 minutes a day, about half an excavator.

## Slide 10: Then, make the better way the normal way
Chart: Minutes per excavator: every step ends up under takt
| OP10 | OP20 | OP30 | OP40 | OP50 | OP60
Before | 39 | 36 | 42 | 38 | 27 | 30
After | 33 | 31 | 32.5 | 33 | 30 | 28
Target takt (35 min) | 35 | 35 | 35 | 35 | 35 | 35
Standard work
+0.7 excavator
Probes replace dial gauges, and some drilling moves to OP50, which had time to spare.
Built-in quality
+0.3 excavator
Poka-yoke locators so a frame can't be clamped wrong, plus SPC on the pin bores.
5S and daily kaizen
Keeps it going
Visual boards, daily huddles and a skill matrix, so the gains don't slip back.
Notes: The next three levers turn those improvements into the normal way of working. Lever 4 is standard work and line balancing. A time study gives each operation a standard work chart. Using a Yamazumi chart, we move some non-critical drilling and tapping from OP10 and OP40 to OP50, which had spare time. OP50 goes from 27 to 30 minutes but stays under takt. In-machine probing replaces dial-gauge alignment, and CNC tool paths are tidied up within validated speeds and feeds. Slow set-up drops from 15 to 6 minutes and the cycle from 30 to 29: about 0.7 of an excavator. Lever 5 is built-in quality. Poka-yoke locating pins mean a frame can't be clamped the wrong way. The probe checks critical pin bores before the frame comes off the machine. SPC charts track those bores with a Cpk of at least 1.33, and the machine stops itself on a tool-wear or out-of-tolerance alarm, which is jidoka. Rework falls from 15 to 6 minutes, about 0.3 of an excavator, and fewer defects reach paint and assembly. Lever 6 is 5S, visual management and kaizen: shadow boards at every machine, hour-by-hour output, OEE and Andon on the digital board, daily tier meetings, PDCA kaizen, and a skill matrix so operators can cover for each other. This is what stops the other five from slipping back. The chart shows the result: after the changes, every operation is under the 35-minute takt.

## Slide 11: The result: room for 12.9, so 12 is safe
Chart: Extra excavators per shift, by lever (total +2.9)
| SMED | Standard work | JIT flow | TPM | Built-in quality
Extra excavators | 1 | 0.7 | 0.5 | 0.4 | 0.3
OP30, before and after 12 weeks
Excavators per shift
10
→
12
OEE
66.7%
→
86%
First-pass yield
95.2%
→
98.4%
Even if only 70% of these gains stick, OP30 can still make 12.05 a shift.
Notes: Add it all up and OP30 goes from 10 excavators a shift to a capacity of 12.9. SMED frees 30 minutes, TPM 13, JIT 14, standard work 19 (9 from faster set-up and 10 from the quicker cycle), and built-in quality 9. Each is converted at the new 29-minute cycle. As a check: losses fall from 120 to 45 minutes, so good output is 420 minus 45, divided by 29, which is 12.9. OEE rises to about 86% capability. Changeovers drop from 15 to 5 minutes each, and breakdown loss from 25 to 12 minutes a shift. Scheduled at 12 a shift, OP30 runs at about 80% OEE, which leaves around 7% spare as a safety margin. And it's robust. Even if only 70% of these gains hold, capacity is 12.05, still above target. There's also one upside we haven't counted: a multi-skilled relief operator running OP30 through the two tea breaks would add about 20 minutes, or roughly another 0.7 of an excavator.

## Slide 12: Twelve weeks to twelve a day
Excavators per shift at the end of each phase
10
Weeks 1–2 | Plan
Understand
Gemba walks, time study
Measure OEE at OP30
Form the kaizen team
11
Weeks 3–6 | Do
Quick wins
5S and visual boards
SMED workshop
FIFO lane, kits, jib crane
11.6
Weeks 7–10 | Do
Fix root causes
TPM routines
Probing and quick clamps
Poka-yoke, move drilling
12
Weeks 11–12 | Check & act
Lock it in
Check FPY and Cpk
Freeze standard work
Roll out to OP10, 20, 40
Notes: Here's how we'd roll it out, following Plan, Do, Check, Act. Weeks 1 and 2 are about understanding: Gemba walks, time studies, an OEE baseline at OP30, and a cross-functional kaizen team with production, maintenance, quality, industrial engineering and the operators themselves. Weeks 3 to 6 are quick wins: 5S, visual boards, the SMED workshop at OP30, the FIFO lane, kitting and the jib crane. That should take us to about 11 a shift. Weeks 7 to 10 fix the deeper causes: TPM steps 1 to 3, probing and zero-point clamps, CNC optimisation, poka-yoke and moving drilling to OP50. That gets us to about 11.6. Weeks 11 and 12 lock it in: verify first-pass yield and Cpk, freeze the new standard work, start layered audits and roll out to OP10, OP20 and OP40. By the end, we're at 12.

## Slide 13: Three things we'd like you to remember
It's waste, not speed
Most of the two extra machines come from 75 lost minutes we win back at OP30.
Quality is built in
No inspection step is removed. If quality slips, we stop and fix it first.
The system makes it stick
Standard work and daily kaizen, the Volvo Production System way.
Thank you. Questions?
Notes: To wrap up, three things we'd like you to take away. First, the extra output comes from removing waste, not from rushing. Most of it comes from winning back 75 of OP30's 120 lost minutes, and the rest from a one-minute faster, validated cycle. Second, quality is protected by design. No inspection step is removed, speeds and feeds stay within validated limits, and if first-pass yield drops below 98% or Cpk below 1.33, we stop and fix the problem first. Third, it lasts because of the Volvo Production System culture: teamwork, standard work and getting a little better every day. Thank you for listening. We'd be happy to take your questions.